## Slide 1: ELECTROCHEMICAL METHODS

## Slide 2: CONTENT
INTRODUCTION
PRINCIPLE
IMPORTANT DEFINITIONS AND RELATIONS
MEASURMENT OF CONDCTIVITY
INSTRUMENTATION
CONDUCTOMETRIC TITRATIONS
ADVANTAGES AND DISADVANTAGES OF CONDUCTOMETRIC TITRATIONS
APPLICATIONS OF CONDUCTOMETRIC MEASURMENTS

## Slide 3: ELECTROCHEMICAL METHODS
Electrochemical methods are analytical techniques that use a measurement of potential, charge or current to determine an analyte concentration or to characterize an analytes chemical techniques.
These methods are divided into 5 major groups
Potentiometry
Voltametry
Coulometry
Conductometry
Dielectrometry

## Slide 4: Conductometry
Conductometric analysis is based on the measurement of the electrical conductivity of the solution due to the mobility of cations and anions towards respective electrodes.
The electrical conductivity is entirely due to the movement of ions.
The ability of any ion to transport charge depends on the mobility of the ion.
The mobility of an ion is affected by factors such as:
Number of ions
Charge of ions
Size of ions Temperature

## Slide 5: Principle
Based on the conductance of electrical current through electrolyte solutions similar to metallic conductors.
The electric conductance in accordance with ohms law which states that the strength of current(I) passing through conductor is directly proportional to potential difference and inversely to resistance.
I=V/R
Where I = strength of current
V= potential difference
R= resistance

## Slide 6: DEFINITIONS
Ohms law: According to this law, the strength of current
(I) flowing through a conductor is directly proportional to the potential difference (E) applied across the conductor and inversely proportional to the resistance (R) of the conductor.
I = E/R
Conductance: It implies the ease with which the current flows through conductor, thus the conductance is reciprocal to resistance.
C= I/R

## Slide 7: Definition Cont…
Specific resistance: (ρ) is the resistance offered by a substance of 1cm length and 1sq.cm surface area
Unit of measurement is ohm cm.
Specific conductivity: (kv) is the conductivity offered by a substance of 1cm length and 1sq.cm surface area,
Unit of measurement is mhos cmˉ1
Equivalent conductivity: (λv) is the conductivity of a solution containing equivalent weight of the solute between electrodes 1cm apart and 1sq cm surface area
Unit of measurement is mhos cmˉ1

## Slide 8: Definition Cont….
Molecular conductance: This may be defined as “the conductance of a solution containing 1gm mole of electrolyte when placed between two sufficiently large electrodes placed 1cm apart”
 It is denoted by µv and is measured in mhos

## Slide 9
MEASUREMENT OF CONDUCTANCE
It has already been seen that the measurement of conductance is a measurement of resistance, the Wheatstone bridge method can, therefore, be used for its measurement.

## Slide 10: Conductometric titrations
Determination of end point of a titration with the help of conductivity measurements is termed as conductometric titrations.
In a conductometric titration the titrant is added.
The values of conductivity are then plotted against the volumes of the titrant in c.c.
Since the measured conductivity is a linear function of the concentration of ions present, two lines will be obtained which will intersect each other at a point, known as “End point” or “Equivalence point”

## Slide 11: CONDUCTOMETER

## Slide 12: CONDUCTIVITY METER
BURETTE
CONDUCTIVTY CELL
MAGNETIC STIRRER

## Slide 13: TYPES OF CONDUCTOMETRIC TITRATIONS

## Slide 14: ACID-BASE OR NEUTRAL TITRATIONS
STRONG ACID- STRONG BASE
eg. HCl vs NaOH
STRONG ACID – WEAK BASE
eg. HCl vs NH4OH
WEAK ACID – STRONG BASE
eg. CH3COOH vs NaOH
WEAK ACID – WEAK BASE
eg. CH3COOH vs NH4OH

## Slide 15: STRONG ACID- STRONG BASE
Fall in conductance due to replacement of high conductivity hydrogen ions by poor conductivity of sodium ions.
Rise in conductance due to increase in hydroxyl ions.

## Slide 16: STRONG ACID – WEAK BASE
Fall in conductance due to replacement of hydrogen by ammonium ions
Conductance remain constant due to suppression of NH4OH by NH4Cl.

## Slide 17: WEAK ACID – STRONG BASE:
Initial decrease in conductance followed by increase due to NaOH
Steep rise due to excess of NaOH

## Slide 18: WEAK ACID – WEAK BASE
Increase in conductance due to excess of CH3COOH
Constant conductance due to suppression of NH4OH by CH3COOH

## Slide 20: ADVANTAGES OF CONDUCTOMETRIC TITRATIONS
Does not require indicators since change in conductance is measured by conductometer.
Suitable for coloured solutions.
Since end point is determined by graphically means accurate results are obtained with minimum error.
Used for analysis of turbid suspensions, weak acids, weak bases, mix of weak and strong acids.
Temperature is maintained constant throughout the titration.
This method cab be used with much diluted solutions.
Be seen by eye.

## Slide 21: DISADVANTAGES
Increased levels of salt in solutions masks the conductivity changes in such cases it does not gives accurate results.
Applications of conductometric titrations to redox systems is limited because, high concentration of hydronium ions in the solutions tends to mask the change in conductance.