## Slide 2: Paper Chromatography
In the year (1865) Paper Chromatography (PC) was first introduced by German scientist Christian Friedrich Schonbein. Paper chromatography is considered to be the simplest and most widely used of the chromatographic techniques because of its applicability to isolation, identification and quantitative determination of organic and inorganic compounds.

## Slide 3: Paper Chromatography
It is carried out mainly by the flow of solvents on specially designed filter paper.

## Slide 4: Paper Chromatography
There are two types of paper chromatography, they are:
1. PAPER ADSORPTION CHROMATOGRAPHY
Paper impregnated with silica or alumina acts as adsorbent (stationary phase) and solvent as mobile phase.
2. PAPER PARTITION CHROMATOGRAPHY
Moisture / Water present in the pores of cellulose fibers present in filter paper acts as stationary phase & another mobile phase is used as solvent.

## Slide 5: Principle of Separation (Partition)
Partition:-
The principle of separation is mainly partition rather than adsorption.
Cellulose layers in filter paper contains moisture which acts as stationary phase and organic solvents/buffers are used as mobile phase.
The substances are distributed or partition between to liquid phases. One phase is the water which is held in the pores of filter paper used and other is that of mobile phase which moves over the paper.
Separation of the components depends upon both their solubility in the mobile phase and differential affinity to the mobile phase and stationary phase.

## Slide 6: Principle of Separation (adsorption)
Adsorption:-
The principle can also be adsorption chromatography between solid and liquid phases, where the stationary phase in the solid surface of paper and the liquid phase is of mobile phase.
Paper impregnated with silica or alumina acts as absorbent (stationary Phase) and solvent as mobile phase.

## Slide 7: Adsorption Chromatography
Adsorption chromatography is defined as a type of chromatography where the solute molecules are directly bound to the surface of the stationary phase. These adsorption sites differ in tenacity with regards to the molecules that they bind in their relative abundance. The adsorbent activity is determined by the net effect. Adsorption chromatography uses mobile phase in liquid or gas state and stationary phase in the solid state. Each solute has a balance between the adsorption to the surface of the solid and solubility in the solvent. Therefore, the solvent will move up with the mobile phase, and at a point where a state of equilibrium is reached.
The difference in travelling distances of compounds could be used to identify the particular compound. There are three types of adsorption chromatographic techniques namely, paper chromatography, thin layer chromatography and column chromatography.

## Slide 8: Partition chromatography
Partition chromatography is another type of chromatography that works under the same principle with slight alterations. Similar to other chromatography variances, partition chromatography also contains a stationary phase and a mobile phase.
Both the stationary and mobile phases are liquids. During liquid-liquid separation, a particular compound is separated when it reaches the two immiscible liquid phases that are present under equilibrium conditions. The two liquid phases are the original solvent and the film of solvent that is present in the adsorption column.

## Slide 9: What are the Similarities Between Adsorption and Partition Chromatography?
Both adsorption and partition chromatography are varieties of chromatography
Both types of chromatography function under the same principle of chromatography
Both types are used to separate mixtures of compounds.
Both adsorption and partition chromatography contain stationary and mobile phases.
Adsorption and partition chromatography possess the ability to separate compounds in all three states; gas, liquid and solid.
The mobile phase of both types is in liquid states

## Slide 10: What is the Difference Between Adsorption and Partition Chromatography?
Adsorption vs Partition Chromatography | 
Adsorption chromatography is defined as a type of chromatography in which separation occurs based on adsorption. | Partition chromatography is a type of chromatography in which separation is based on partition.
Extraction | 
Adsorption chromatography is a liquid-solid extraction. | Partition chromatography is a liquid-liquid extraction.
Stationary Phase | 
The stationary phase is in the solid state of adsorption chromatography. | The stationary phase is a liquid state in partition chromatography.
Developments | 
Adsorption chromatography was not further developed. | Partition chromatography leads to the development of other types of chromatography.

## Slide 11: Theory
Two types of forces operate when a drop of solution is applied on the filter paper and treated with the mobile phase.
Propelling force It tries the substances in the direction of the flow of solvent. The depends on:-
1. The rate of solvent flow 2. the solubility of the substances in the solvent.
3. The component with higher solubility in the mobile phase will move faster along the filter than less soluble component.
2. Retarding forces

## Slide 12: PAPER CHROMATOGRAPHY
PRACTICAL REQUIREMENTS
1)Stationary phase & papers used
2)Application of sample
3)Mobile phase
4)Development technique
5)Detecting or Visualizing agents

## Slide 13: Paper Chromatography
A wide variety of paper are available depending in their size, shape, porosities, thickness and chemical treatments. Generally paper is composed of randomly directed cellulose fibers. Cellulose itself is a network of polymeric carbohydrate chains possessing hydrophilic character and cross linked stable hydrogen bonded system.

## Slide 14: PAPER CHROMATOGRAPHY
Modified Papers – acid or base washed filter paper, glass fiber type paper.
Hydrophilic Papers – Papers modified with methanol, glycol, glycerol etc.
Hydrophobic papers – acetylation of OH groups leads to hydrophobic nature.
Impregnation of silica, alumna, or ion exchange resins can also be made.

## Slide 15: PAPER CHROMATOGRAPHY
STATIONARY PHASE AND PAPERS USED
Whatman filter papers of different grades like No.1, No.2, No.3, No.4, No.20, No.40, No.42 etc are used. In general this paper contains 98-99% of α-cellulose, 0.3 – 1% β-cellulose
Factors that governs the choice of paper:
Nature of Sample and solvents used.
Based on Quantitative or Qualitative analysis.
Based on thickness of the paper.

## Slide 16: PAPER CHROMATOGRAPHY
Modified Papers – acid or base washed filter paper, glass fiber type paper.
Hydrophilic Papers – Papers modified with methanol, formamide, glycol, glycerol etc.
Hydrophobic papers – acetylation of OH groups leads to hydrophobic nature, hence can be used for reverse phase chromatography.
Impregnation of silica, alumna, or ion exchange resins can also be made.

## Slide 17: PREPARATION OF PAPER
Cut the paper into desired shape and size depending upon work to be carried out.
The starting line is marked on the paper with an ordinary pencil 5cm from the bottom edge.
On the staring line marks are made 2cm apart from each other.

## Slide 18: PAPER CHROMATOGRAPHY
Preparation of the solution
Choice of suitable solvent for making solution is very important. Pure solutions can be applied direct on the paper but solids are always dissolved in small quantity of a suitable solvent.
Biological tissues are treated with suitable solvents and their extracts obtained. Proteins can be precipitated with alcohol and salts can be removed by treatment with ion exchange resin.

## Slide 19: PAPER CHROMATOGRAPHY
APPLICATION OF SAMPLE
The sample to be applied is dissolved in the mobile phase and applied as a small spot on the origin line, using capillary tube or micropipette.
very low concentration is used to avoid larger zone
The spot is dried on the filter paper and is placed in developing chamber.

## Slide 20: Choice of the Solvent
The commonly employed solvents are the polar solvents, but the choice depends on the nature of the substance to be separated.
If pure solvents do not give satisfactory separation, a mixture of solvents of suitable polarity may be applied.

## Slide 21: PAPER CHROMATOGRAPHY
MOBILE PHASE
Pure solvents, buffer solutions or mixture of solvents
Examples- Hydrophilic mobile phase
Isopropanol: ammonia:water 9:1:2
Methanol : water 4:1
N-butanol : glacial acetic acid : water 4:1:5
Hydrophobic mobile phases
dimethyl ether: cyclohexane
kerosene : 70% isopropanol

## Slide 22: CHROMATOGRAPHIC CHAMBER
The chromatographic chamber are made up of many materials like glass, plastic or stainless steel.
Glass tanks are preferred most. They are available in various dimensional size depending upon paper length and development type.
The chamber atmosphere should be saturated with solvent vapor.

## Slide 23: PAPER CHROMATOGRAPHY
DEVELOPMENT TECHNIQUE
Paper is flexible when compared to glass plate used in TLC, several types of development are possible which increases the ease of operation.
The paper is dipped in solvent in such a manner that the spots will not dip completely into the solvent.
The solvent will rise up and it is allowed to run 2/3rd of paper height for better and efficient result.

## Slide 24: Developing Techniques
Based upon the development of the chromatogram, paper chromatography are four Types
Ascending Chromatography
Descending Chromatography
Paper Chromatography
Radial Chromatography
Two dimensional Chromatography

## Slide 25: PAPER CHROMATOGRAPHY
Different types of development tech. are
1) ASCENDING DEVELOPMENT (go up)
Like conventional type, the solvent flows against gravity. The spots are kept at the bottom portion of paper and kept in a chamber with mobile phase solvent at the bottom.

## Slide 27: PAPER CHROMATOGRAPHY
2) DESCENDING TYPE (a downward slope)
This is carried out in a special chamber where the solvent holder is at the top. The spot is kept at the top and the solvent flows down the paper.
In this method solvent moves from top to bottom so it is called descending chromatography.
ADVANTAGE IS THAT, DEVELOPMENT IS FASTER

## Slide 29: PAPER CHROMATOGRAPHY
3)ASCENDING – DESCENDING DEVELOPMENT
A hybrid of above two technique is called
ascending-descending chromatography.
Only length of separation increased, first ascending takes place followed by descending

## Slide 30: PAPER CHROMATOGRAPHY
4)CIRCULAR / RADIAL DEVELOPMENT
Spot is kept at the centre of a circular paper. The solvent flows through a wick at the centre & spreads in all directions uniformly.

## Slide 31: PAPER CHROMATOGRAPHY
5) TWO DIMENSIONAL DEVELOPMENT
In this method the paper is developed in one direction and after development, the paper is developed in the second direction allowing more compounds to be separated into individual spots.
in the second direction, either same solvent/different solvent system can be used for development.

## Slide 32: TWO DIMENSIONAL DEVELOPMENT

## Slide 34: PAPER CHROMATOGRAPHY
DRYING OF CHROMATOGRAM
• After the solvent has moved a certain distance for certain time the chromatogram is taken out from the tank & position of the solvent front is marked with a pencil.
They are dried by cold or hot air depending on volatility of solvents. A simple hair dryer is a convenient device to dry chromatograms.

## Slide 35: PAPER CHROMATOGRAPHY
DETECTING / VISUALISING AGENTS
If the substance are colored they are visually detected easily.
But for colorless substance, Physical and chemical methods are used to detect the spot.
Non specific methods ( Physical methods)
E.g. iodine chamber method,
UV chamber for fluorescent compounds – at 254 or at 365nm.

## Slide 36: (b) Specific methods (Chemical methods) or Spraying method - examples,
Ferric chloride
Ninhydrin in acetone
Dragendroff’s reagents
3,5 dinitro benzoic acid
Phenolic comp. & tannins
Amino acids
Alkaloids
Cardiac glycosides

## Slide 37: Following detecting tech. can also be categorized as
1) Destructive techniques
Specific spray reagents, samples destroyed before detection e.g. – ninhydrin reagent
2) Non-destructive techniques
For radio active materials - Geiger Muller counter
UV chamber, iodine chamber
QUANTITATIVE ESTIMATIONS
The method can be divided into two main groups
1. Direct techniques-
2. Indirect techniques-

## Slide 38: PAPER CHROMATOGRAPHY
Direct Measurement Method
(i) Comparison of visible spots
A rough quantitative measurements
Component in a mixture can be carried out by comparing the intensity and size of the spot with a standard substance.
(ii) Photo densitometry
The method is used with the chromatograms of colored compound, instrument which measures quantitatively the density of the spots.

## Slide 39: PAPER CHROMATOGRAPHY
(iii) Fluorimetry
The compound to be determined by fluorimetry must be fluorescent or convertible into fluorescent derivatives.
(iv) Radiotracer Method
The compound containing radioactive element is labeled and treated with locating reagent. Using Geiger Muller counter.
(v) Polarographic & Conductometric methods
Used to measure the amount of material in the spot

## Slide 40: PAPER CHROMATOGRAPHY
Indirect Measurement Method
In this technique, the spots are cut into portions and eluted with solvents. This solution can be analyzed by any techniques of analysis like spectrophotometry, electrochemical methods, etc.

## Slide 41: Rf VALUE (Retardation Factor)
In paper chromatography the results are represented by Rf value which represent the movement or migration of solute relative to the solvent front.
The Rf value is calculated as :
Distance travelled by the solute
Distance travelled by the solvent front

## Slide 42: Factors affecting Rf VALUE
i. The temperature
ii. The purity of the solvents used
iii. The quality of the paper, adsorbents & impurities present n the adsorbents
iv. Chamber saturation techniques, method of drying & development
v. The distance travelled by the solute & solvent
vi. Chemical reaction between the substances being partitioned.
vii. pH of the solution

## Slide 43: Sources of Error
1. Error during application of the spots
Apply minimum volume of the concentrated solution in order to avoid diffusion through the paper which leads to poor separation
Spots should be approximately of the same diameter.
2. Development
Improper adjustment of the paper in the tank leads to this error so the paper should be held vertically.
Do chamber saturation
3. Detection
The spraying methods affect the final result

## Slide 44: APPLICATIONS
Separation of mixtures of drugs
Separation of carbohydrates, vitamins, antibiotics, proteins, etc.
Identification of drugs
Identification of impurities
Analysis of metabolites of drugs in blood , urine ….
ADVANTAGES OF Paper Chromatography
Simple ,rapid ,inexpensive ,excellent resolving power
PRECAUTIONS IN Paper chromatography
Establishing the vapor solvent equilibrium
Stability of solvent mixture is first ensured

## Slide 50: Reaction monitoring
In a chemical reaction over a period of time the concentration of reactants decreases whereas the concentration of products increases. Developing the chromatogram over different time intervals by spotting the reactants can give a fair idea on the progress of reaction. Traditionally the technique was used for qualitative monitoring but availability of densitometers made quantitative estimations possible. However, rapid methods using spectroscopic techniques are limiting the application of paper chromatography as a reaction monitoring option

## Slide 51: Isolation & Purification
Paper chromatography has been put to use as a purification and isolation technique for components of mixtures. The separated components on the paper are cut, dissolved in suitable solvents and their absorption characterised at specific wavelengths using spectrophotometric methods. This approach is being superseded by techniques such as Preparative HPLC.

## Slide 52: Pharmaceuticals
Paper chromatography provides useful information on development of new drug molecules, reaction completion and progress of manufacturing processes. It also offers a cost-effective alternative to monitoring the active ingredients in drug forms administered in bio-analytical studies. Its main contribution is when the quantity of sample available is in minute amounts.
In a subsequent article some reasons will be presented for justification of continued popularity of paper chromatography in the face of tough competition from more advanced chromatographic techniques.

## Slide 53: Forensics science
A forensic scientist is often faced with a severe limitation on the quantity of sample available for analysis Paper chromatography offers a viable analysis option for samples available in milligrams or micro-litre quantities.
The major applications are for identification and comparison against reference standards for drugs and their metabolites in viscera, explosive residues from blast sites, inks used in forgery of documents and paint pigments investigations in hit and run road accident cases.

## Slide 54: Foods
Paper chromatography has been primaly used for analysis of food colours in synthetic drinks and beverages, ice creams, jams & jellies, sweets, etc. Colours both natural and synthetic are added to foods to improve their acceptability and to make them more popular. Only edible colours are permitted for use so identification and quantification becomes all the more important to ensure that no non- permitted colouring agents are added to the foods.