## Slide 1
TLC
Khalid Mahmoud

## Slide 2
THIN LAYER CHROMATOGRAPHY (TLC)

## Slide 3
Mikhail Tsvet
Born 14 May 1872
Asti, Italy
Died 26 June 1919 (age 47)
Nationality Russia
Fields Botany
Mikhail Semyonovich Tsvet (Михаи́л Семёнович Цвет, also spelled Tsvett, Tswett, Tswet, Zwet, and Cvet) (1872–1919) was a Russian-Italian botanist who invented Adsorption chromatography.

## Slide 4: Invention of Chromatography by M. Tswett
Ether
CaCO3
Chlorophyll
Chromatography
Colors
Notes: The Russian-Polish botanist M. Tswett is generally recognized as the first person to establish the principles of chromatography.
In a paper he presented in 1906, Tswett described how he filled a glass tube with chalk powder (CaCO3) and, by allowing an ether solution of chlorophyll to flow through the chalk, separated the chlorophyll into layers of different colors. He called this technique “chromatography”.

## Slide 5: Comparing Chromatography to the Flow of a River...
Base
Water flow
Light leaf
Heavy stone
Notes: Chromatography can be often compared to the flow of a river.
A river consists of a stationary riverbed and water that continuously moves in one direction. What happens if a leaf and a stone are thrown into the river? The relatively light leaf does not sink to the bottom, and is carried downstream by the current. On the other hand, the relatively heavy stone sinks to the bottom, and although it is gradually pulled downstream by the current, it moves much more slowly than the leaf.
If you stand watch at the mouth of the river, you will eventually be able to observe the arrival of the leaf and the stone. However, although the leaf will arrive in an extremely short time, the stone will take much longer to arrive.
This analogy represents the components of chromatography in the following way:
  River: Separation field
  Leaf and stone: Target components of sample
  Standing watch at the river mouth: Detector

## Slide 6
Thin layer chromatography (TLC) is a chromatography technique used to separate mixtures.
Thin layer chromatography is performed on a sheet of glass, plastic, or aluminum foil, which is coated with a thin layer of adsorbent material, usually silica gel, aluminum oxide, or cellulose. This layer of adsorbent is known as the stationary phase.
PRINCIPLE
The principle of separation is adsorption. One or more compounds are spotted on a thin layer of adsorbent coated on a chromatographic plate. The mobile phase solvent flows through because of capillary action. The components move according to their affinities towards the adsorbent. The component with more affinity towards the stationary phase travels slower. The component with lesser affinity towards the stationary phase travels faster. Thus the components are separated in a thin layer chromatographic plate based on the affinity of the components towards the stationary phase.

## Slide 7
ADVANTAGES OF TLC over paper chromatography:-
Simple method and cost of the equipment is low
Rapid technique and not time consuming like column chromatography
Separation of mg of the substances can be achieved
Any type of compound can be analyzed
Efficiency of separation: Very small particle size can be used which increases the efficiency of separation. Flow rate is not altered because of the particle size since it is not a closed column. It is planar type having thing layer of adsorbent
Detection is easy and not tedious
Capacity of the thin layer can be altered. Hence analytical and preparative separations can be made
Corrosive spray reagents can be used without damaging the plates
Needs less solvent, stationary phase and time for every separation when compared to column chromatography

## Slide 8
PRACTICAL REQUIREMENTS
Stationary phase
Glass plates
Preparation and activation of TLC plates
Application of sample
Development tank
Mobile Phase
Development technique
Detecting or visualizing agents

## Slide 10: Steps Involving in TLC
Sample Preparation
Selection of chromatography layer
Pre-washing
Pre-conditioning
Application of sample
Chromatography development
Detection of spots
Scanning & documentation

## Slide 11
1) STATIONARY PHASE
There are several adsorbents which can be used as stationary phase. Some of the stationary phases, their composition and the ratio in which they have to be mixed with water or other solvents to form a slurry for preparing thin layer chromatographic plates are given in the following table:

## Slide 12
2) GLASS PLATES
Glass plates which are specific dimensions like 20 cm X 20 cm (Full plate), 20 X 10 cm(Half plate), 20 cm X 5 cm (Quarter plate) can be used. These dimensions are used since the width of the commercially available TLC spreader is 20 cm.
Microscopic slides can also be used for some applications like monitoring the progress of a chemical reaction. The development time is much shorter like 5 minutes.
Glass plates of different dimensions can also be used when the TLC plates are prepared without the use of TLC spreader. In general, the glass plates should be of good quality and should withstand temperatures used for drying the plates.

## Slide 13
3) PREPARATION AND ACTIVATION OF TLC PLATES
The slurry, which is a mixture of stationary phase and water is prepared by using the ratio mentioned earlier. After preparing the slurry, the TLC plates can be prepared by using any one of the following techniques; pouring, dipping, spraying and spreading
Pouring technique: the slurry is prepared and poured on to a glass plate which is maintained on a leveled surface. The slurry is spread uniformly on the surface of the glass plate. After setting, the plates are dried in an oven is used for spotting. The disadvantage is that uniformity in thickness can not be ensured.

## Slide 14
Dipping technique: two plates (either of standard dimensions or microscopic slides) are dipped in to slurry and are separated after removing from slurry and later dried. The disadvantage is that a larger quantity of slurry is required even for preparing fewer plates.
Spraying technique: resembles that of using a perfume spray on a cloth. The suspension of adsorbent or slurry is sprayed on a glass plate using a sprayer. The disadvantage is that the layer thickness cannot be maintained uniformly all over the plate.

## Slide 15
Spreading: is the best technique where a TLC spreader is used. The glass plates of specific dimensions (20cm X 20cm/10 cm/5cm) are stacked on a base plate. The slurry after preparation is poured inside the reservoir of TLC spreader. The thickness of the adsorbent layer is adjusted by using a knob in the spreader. Normally a thickness of 0.25cm is used for analytical purpose and 2 mm thickness for preparative purpose. Then the spreader is rolled only once on the plate. The plates are allowed for setting(air drying). This is done to avoid cracks on the surface of adsorbent. After setting, the plates are activated by keeping in an oven at 100oC to 120oC for 1 hour

## Slide 16
Activation of TLC plates is nothing but removing water/moisture and other adsorbed substances from the surface of any adsorbent, by heating at high temperature so that adsorbent activity is retained. The activated plates can be stored in thermostatically controlled oven or in desiccator and can be used whenever required.

## Slide 17
4) APPLICATION OF SAMPLE
Usually to get good spots, the concentration of the sample or standard solution has to minimum, 2-5ml of a 1% solution of either standard or test sample is spotted using a capillary tube or micropipette. The spots can be placed at random by using a template, with markings. The spots should be kept at least 2cm above the base of the plate and the spotting area should not be immersed in the mobile phase in the development tank. At least 4 spots can be spotted plate (20cm X 5cm).

## Slide 18: 5) DEVELOPMENT TANK
For the purpose of development, a developing tank or chamber of different sizes to hold TLC plates of standard dimensions are used. These require more solvents for developing the chromatogram. When a new method is developed, it is better to develop in glass beakers, specimen jars etc., to avoid more wastage of solvents. When developed method or standard method is used, it is better to used development tank. New type of development tanks have hump in the middle, which require less solvent. The development chamber or tank should be line inside the filter paper moistened with the mobile phase so as to saturate the atmosphere. If this kind of saturation of the atmosphere is not done “edge effect” occurs where the solvent front in the middle of TLC plate moves faster than that of the edge. Therefore the spots are disorted and not regular.

## Slide 19: 6) MOBILE PHASE
The solvent or the mobile phase used depends upon various factors as mentioned in column chromatography. Some of the factors are:
  Nature of the substances to be separated
  Nature of the stationary phase used
  Mode of chromatography (Normal phase or reverse phase)
  Separation to be achieved – Analytical or preparative
Pure solvents or mixture of solvents are used. The following gives a list of solvents (of
increasing polarity)
Petroleum ether, Carbon tetrachloride, Cyclohexane, Carbondisulfide, Ether, Acetone, Benzene, Toluene, Ethyl acetate, Chloroform, Alcohols, Water, Pyridine, organic acids, inorganic acid.

## Slide 20
7) DEVELOPMENT TECHNIQUE
Different development techniques are used for efficient separations. They are
One dimensional development (vertical)
Two dimensional development
Horizontal development
Multiple development

## Slide 21
1. One dimensional development (vertical)
Like conventional type, the solvent flows against gravity. The spots are kept at the bottom
portion of paper and kept in a chamber with mobile phase solvent at the bottom
2. Two dimensional technique
This technique is similar to 2-Dimensional TLC. The paper is developed in one direction and after development, the paper is developed in the second direction allowing more compounds or complex mixtures to be separeted into individual spots. In the second direction, either the same solvent or different solvent system can be used for development.

## Slide 22: 8.Detecting agent
•
After the development of chromatogram, the spots should be visualised. Detecting coloured spots can be done visually, But for detecting colourless spots, any one of the following techniques can be used.
Non specific method: Where the number of spots can be detected but not exact nature of compound
Example
  Iodine Chamber Method: Where brown or amber spots are observed when the paper is kept tank with few iodine crystals at the bottom
  UV Chamber for flourescent compounds: When compounds are viewed under UV chamber at 245 nm or at 365 nm flourescent compounds can be detected.

## Slide 23: 8.Detecting agent
b. Specific methods: Specific spray reagents or detecting agents visualizing agents are used to find out the nature of compounds for identification purposes
-
For phenolic compounds and tannins
-
For amino acids
-
For alkaloids
Examples
Ferric chloride
Ninhydrin in acetone
Dragendroff’s reagent
3,5-Dinitro benzoic acid
-
For cardiac glycosides
v. 2,4-Dinitrophenyl hydrazine –
For aldehydes and ketones

## Slide 24: Quantitative analysis
Direct technique: Densitometer is an instrument which measures quantitatively the density of the spots. When the optical density of the spots for the standard and test solution are determined, the quantity of the substance can be calculated.
Indirect technique: In this technique, the spots are cut into portions and eluted with solvents. This solution can be analysed by any conventional techniques of analysis like spectrophotometry, electrochemical methods etc.,

## Slide 25: Qualitative analysis
Rf Value
The Rf value (Retardation factor) is calculated for identifying the spots i.e. in Qualitative analysis. Rf value is the ratio of distance travelled by the solute to the distance travelled by the solvent front.
The Rf value ranges from 0 to 1. But ideal values are fro 0.3 to 0.8. Rf value is constant for every compound in a particular combination of stationary and mobile phase. When the Rf value of a sample and reference compound is same, the compound is identified.

## Slide 26: Qualitative analysis
Rx Value
Rx value is nothing but the ratio of distance travelled by the sample and the distance travelled by standard. Rx value is always closer to 1.

## Slide 27: Field of Applications
Chart: 
| Field Of Applications | Medicine | Pharmacy | Environment | Food | Chemistry | TLC mehods
 | 26 | 25 | 11 | 18 | 6 | 14

## Slide 28: APPLICATIONS
Pharmaceutical Researches
Bio­medical Analysis
Clinical Analysis
Environmental Analysis
Food Industry
Therapeutic drug monitoring to determine concentration of drug
and it’s metabolite in blood, urine etc
Analysis of environmental pollutions levels
Quantitative determination of prostaglandin’s and thromboxanes
in plasma
Analysis of nitrosoamines in food and body fluids
Determination of sorbic acid in wine
Characterization of hazards in industrial waste